## Slide 1: Administrative
Quiz2 grades posted on Trunk. Mean 18.6 out of 22
Matlab3 posted on Trunk. Mean 90.8
  Matlab2 grades will be posted by end of week
Matlab 5 is due next Thursday, but going over it may help with Exam 2 prep; posted on Trunk
Exam 2 is 1 week from today. Review session- Monday or Tuesday evening?
Review where we are in class

## Slide 2: EE-125: Digital Signal Processing Finish up Spectrograms FIR Filter Design 1 Professor Tracey

## Slide 3: First… some review of spectrum estimation
Spectrogram examples
  Same tradeoffs as before: windows with low sidelobes gives wider mainlobe (thus worse resolution)
  New tradeoff: windows that are short in time give improved time resolution but worse frequency resolution
Posted a review article on multitaper spectrum estimation on Trunk. Not covered on tests or HW, but is good to know about
  Can be used for periodograms or smoother spectrograms, when signal is time-varying but random

## Slide 4: “Big picture” on FIR filters
FIR filters are nice because they can have linear phase / constant group delay, though at the cost of needing more coefficients than IIR (as seen in MATLAB3)
The computational load of FIR filters can be reduced by doing FFT-based filtering (circular convolution = linear convolution) (MATLAB4).
You’ll design FIR filters in MATLAB6 (the last Matlab)

## Slide 5: FIR filter design …
Basic idea of FIR filter design:
  Decide on the ideal frequency response H(w) (LPF, HPF, etc)
  Pick a form for the filter that guarantees linear phase FIR
  Find the coefficient weights that best match H(w)
Last step usually involves trading off fast frequency transitions to get lower responses elsewhere
Three main design approaches:
  Window method
  Frequency sampling
  Optimization of a cost function

## Slide 6: Filter response specifications

## Slide 7: Outline
Linear-phase FIR filters: symmetric and anti-symmetric (P&M section 10.2.1)
Filter design by windowing (P&M 10.2.2)
  Rectangular windows
  Triangle/Bartlett window (mostly for demonstration)
  Hann (or Hanning)window family (used very often)
  Many others….Blackman, Kaiser
Filter design by frequency sampling (P&M 10.2.3)
  Simple versions
  More optimal

## Slide 8: Four basic FIR forms that give linear or generalized linear phase

## Slide 9: Four basic FIR forms that give linear or generalized linear phase
Symmetric around “sample” 2.5
Symmetric around
sample 3

## Slide 10: Filter restrictions
Symmetric filters (Types I and II) naturally have H(w) that involves cos(w*something)
Antisymmetric filters (Types III and IV) naturally have H(w) that involves sin(w*something)
Type II filters always have a zero at z=-1, so can’t be used to design a highpass
Type III filters always have a zeros at z=-1 and z = 1, so can’t be used to design a highpass, lowpass, or bandstop
Type IV (even, antisymmetric) always has zero at z = 1, so can’t be used to design a lowpass

## Slide 11: Filter restrictions
Symmetric filters (Types I and II) naturally have H(w) that involves cos(w*something)
Antisymmetric filters (Types III and IV) naturally have H(w) that involves sin(w*something)
Type II filters always have a zero at z=-1, so can’t be used to design a highpass
Type III filters always have a zeros at z=-1 and z = 1, so can’t be used to design a highpass, lowpass, or bandstop
Type IV (even, antisymmetric) always has zero at z = 1, so can’t be used to design a lowpass
This is why Matlab’s fir1 changed the filter order when you tried to design a 51’st order (52 point long) highpass

## Slide 12: FIR filter design …
Basic idea of FIR filter design:
  Decide on the ideal frequency response H(w)
  Pick a form for the filter that guarantees linear phase FIR
  Find the coefficient weights that best match H(w)
Last step usually involves trading off fast frequency transitions to get lower responses elsewhere
Three main design approaches:
  Window method
  Frequency sampling
  Optimization of a cost function

## Slide 13: Window design considerations
The main issues are main lobe width and sidelobe height
Main lobe determine how ‘smoothed’ the desired response is
  Thus ideally, main lobe would be very narrow
  This generally implies higher M
The sidelobe determines ‘ringing’ in frequency
  High sidelobes mean less attenuation of undesired frequencies
  High frequency sidelobes result from sharp discontinuities in time
Rectangular window: narrowest mainlobe, but high sidelobes
Other windows; wider mainlobe but lower sidelobes
  All are linear phase
  All have smaller mainlobe as M increases (just like rect)
  Design is generally trial-and-error

## Slide 14: Some possible filters
For lots of details on window types, see https://ccrma.stanford.edu/~jos/sasp/sasp.html

## Slide 15: In detail….
Triangle/Bartlett filter – basically convolve two boxcars
Hamming family: multiply rectangular window by one period of a cosine.
  General form is: w(n) = rect(n)*[a+2bcos(2pn/M)]
  If a=0.5 and b=0.25, we get a Hanning or raised cosine
  If we chose a,b to cancel the biggest sidelobe, we get Hamming – quick transition to low sidelobes, then flat
If we add multiple cosines, we get the Blackman family of windows.
Many, many windows to choose from